## Slide 7
計算都合上配置する、物理現象のシミュレートとは直接関係の無いコンポーネントの配置を最初から考え過ぎないこと。
これらのコンポーネントの選択が、物理現象のコンポーネントからなるモデルを大きく覆すは無いので、必要に応じて後から追加すれば良い。
並べ方を無造作ではなく、ある程度実物の形に合わせたものか、機能的な繋がりを示すものにしておく。次手順でコンポーネント同士を接続した後に見通しが悪いモデルになるのを防ぐ。
→左から右への流れ。
→圧送機器、流路抵抗、流量調整弁の順に要素が並ぶ。
ライブラリブラウザ上のコンポーネントをDrag&drop = C++などコーディングにおける、インスタンス生成にあたる作業。
-. 各々のコンポーネントの機能・物理現象・インターフェイスをある程度把握しておく必要が有る。
-. 配置時インスタンスの名前を設定する。後から設定変更も可能
-. アイコンの大きさ、向きを変更可能。
Diagram Viewを表示させるボタン
ライブラリブラウザ
＝コンポーネント一覧

## Slide 9
ソースコードチェックの結果の、variables数とequation数が表示される。
エラーが有る場合、Message Browserにエラー内容が表示される。
ソースコードチェックのボタン

## Slide 10
シミュレーション時間や記録インターバル、その他ソルバに関する設定を行うウィンドウ。
尚、「OK」を押すとそのままコンパイル＆シミュレーションが始まる。
シミュレーション設定を開くボタン

## Slide 11
Plotするvariableを選択する。
「Plotting」を選択してplot画面を表示する。

## Slide 15
-. Flow path consists single pipe.
-. Pipe is composed of “resistance” part and “capacitance” part internally.
-. Pipe has 5 “resistances” and “capacitance”.
-. “Resistance” and “capacitance” lines up one another.
-. Entire pipe receives heat from outside of flow path.
-. Pressure drop and heat receive occur at the same time in single component.
-. Still discretized model. Pressure drops and heat receive occur separately in component.
-. Replicate signal into vector of signal.
-. Heat flow source seems single component. However, there are 5(number of discrete sections of pipe) instances so as to provide heat to 5 heat ports.
-. Divide whole heat flow into pipe by 5 (number of discrete sections of pipe).
-. Place volumes to observe fluid states before and after pipe.

## Slide 16
Input:
Total of heat flow rate injected into fluid system.
Input:
Heat flow rate from each “prescribedHeatFlow1”.

## Slide 17
Output:
Specific enthalpy of fluid before pipe.
Output:
Specific enthalpy of fluid after pipe.
Output:
-. Specific enthalpy of fluid at each volume within pipe.
-. The specific enthalpy of last volume is equal to that of after pipe.

## Slide 18
Output:
Temperature of fluid before pipe.
Output:
Temperature of fluid after pipe.
Output:
-. Temperature of fluid at each volume within pipe.
-. Temperature of last volume is equal to that of after pipe.

## Slide 19
Output:
-. Pressure drop at each segment within pipe.
-. The pressure drop decreases as goes downstream due to temperature rise caused by heat injection.

## Slide 23
-. Flow path consists of 2 pipes.
-. Each pipe is composed of “resistance” part and “capacitance” part.
-. First pipe receives heat from outside of flow path.
-. In this example, it is defined that heat receive occurs AFTER pressure drop of pipe. Definition of BEFORE or AFTER influence on pressure drop because fluid density and viscosity changes.
-. If it is desired that heat receive and pressure drop occurs simultaneously, deploy “DynamicPipe” and define sections as many as possible (Example of “DynamicPipe” will be in “FlowWithHeating_ex02”).
-. Pressure drop in pipe1 is affected by change of density and viscosity due to heat receive upstream.

## Slide 24
Input:
Heat flow rate injected into fluid system.

## Slide 25
Output:
Specific enthalpy of fluid in the volume where heat is injected into fluid system.

## Slide 26
Output:
Temperature of fluid in the volume where heat is injected into fluid system.

## Slide 27
Output:
Pressure drop in pipe1 (pipe downstream of heat injection).

## Slide 28
Output:
Density of fluid at the entrance of pipe1 (pipe downstream of heat injection).

## Slide 29
Output:
Fluid density vs. fluid Temperature.

## Slide 30
Output:
Viscosity of fluid at the entrance of pipe1 (pipe downstream of heat injection).

## Slide 31
Output:
Fluid viscosity vs. fluid temperature.

## Slide 32
Output:
Fluid velocity at the entrance of pipe1 (pipe downstream of heat injection).

## Slide 33
Output:
Reynolds number at the entrance of pipe1 (pipe downstream of heat injection).

## Slide 35
PumpAsTurbine_ex02

## Slide 37
PumpAsTurbine_ex01

## Slide 39
pumpingSystem_ex01

## Slide 40
Pipe= Flow resistance.
-. Fluid pressure drops through it.
Measure fluid power of pump.
Figure out mechanical power supplied to pump.
= (fluid power) / eff.
Centrifugal pump
-. Constant efficiency.
-. Mechanical interface is rotational speed signal.

## Slide 41
Input:
mechanical rotary speed of pump.

## Slide 42
Output:
Volumetric flow rate through pump.

## Slide 43
Output:
pump discharge pressure.

## Slide 44
Output:
Pump’s volumetric flow rate vs. mechanical rotation speed.

## Slide 45
Output:
-. (pump.V_flow)*dP
-. Increase in “flow power”
Output:
-. Mechanical power consumed by pump.
-. (pump.V_flow)*dP / pump.eta
-. 2 variables are equal.

## Slide 46
Output:
mechanical power consumption of pump vs. mechanical rotation speed.

## Slide 48
体積流量 [m^3/s]
揚程 [m]
-. 定格回転数における、揚程 vs. 体積流量の特性カーブを与える必要が有る。
-. MSLには２次カーブと多項式カーブを与えるfunctionが用意されている。
pumpingSystem_ex01では最もシンプルな２次カーブを用いる。
*ユーザー定義のカーブfunctionを用いて呼び出すことも可能。
機械回転数 [rpm]
体積流量 [m]
揚程 [m]
{定格回転数, 定格体積流量}
{定格回転数, 定格揚程}
機械回転数 [rpm]
redeclare function flowCharacteristic = Modelica.Fluid.Machines.BaseClasses.PumpCharacteristics.quadraticFlow(V_flow_nominal = {0, 0.25, 0.5}, head_nominal = {100, 60, 0})
定格点のparameterを基に
体積流量=k*機械回転数
として算出(スケール)される。
定格点のparameterを基に
体積流量=k*(機械回転数)^2
として算出（スケール）される。
非定格点の体積流量、揚程の算出
体積流量、揚程の特性の与え方
下記の記述により、特性モデルにMSL収録の２次カーブfunctionを用いることを設定すると共に、２次カーブを成す３点の値をparameterとして与える

## Slide 49
断熱効率特性の与え方
体積流量 [m^3/s]
断熱効率 [nond]
定格回転数における効率カーブを与える。
MSLには効率を一定とするfunctionしか用意されていないため、カーブを与えたい場合はユーザー定義functionを作成する必要が有る。
pumpingSystem_ex01では、簡略化のため、定格回転数における断熱効率を一定とするようparameter設定する。
redeclare function efficiencyCharacteristic = Modelica.Fluid.Machines.BaseClasses.PumpCharacteristics.constantEfficiency(eta_nominal = 0.9)
下記の記述により、特性モデルに効率固定値のfunctionを用いることを設定すると共に、固定値として設定する効率値を与える。

## Slide 50
pumpingSystem_ex02

## Slide 52
pumpingSystem_ex03

## Slide 53
“Prescribed pump” is replaced with “pump”
The valve for flow control is added. The valve type is the simplest one.
The components so as to provide mechanical rotational speed (in [rpm]) to flange connector are added.

## Slide 54
Input:
mechanical rotary speed of pump.

## Slide 55
Input:
opening of linear valve.

## Slide 56
Output:
Volumetric flow rate through pump.

## Slide 57
Output:
Pump’s volumetric flow rate vs. mechanical rotation speed.

## Slide 58
Output:
pump discharge pressure.

## Slide 59
Output:
Mechanical power consumed by pump.

## Slide 60
Output:
Torque into flange of pump.

## Slide 61
Output:
mechanical power consumption of pump vs. mechanical rotation speed.

## Slide 62
Output:
pressure difference of valve vs. mass flow rate via valve.
Increase in pump rotation speed.
Close of valve (from 1 to 0.5).
If pump speed is reduced.
If pump speed is increased.

## Slide 64
Pipe= Flow resistance.
-. Fluid pressure drops through it.
Input (boundary cond.):
-. mass flow rate with ramp in time. Increase it gradually.
-. Inlet temperature with fixed value.
Input (boundary cond.):
-. Outlet pressure with fixed value.
Output of interest:
-. Inlet pressure.
Volumes
-. In order to see the temperature and enthalpy change across the pipe.
Output of interest:
-. Outlet temperature.

## Slide 65
Input:
mass flow rate flowing through pipe.

## Slide 66
Output:
Fluid pressure of pipe inlet.
It increases as mass flow rate increases.

## Slide 67
Output:
Specific enthalpy at inlet.
Output:
Specific enthalpy at outlet.
It is same value as inlet owe to enthalpy conservation.
The “delay” occurs due to volume effect (storage of mass and energy).

## Slide 68
Output:
Temperature at inlet.
Output:
-. Temperature at outlet.
-. It is slightly greater than that of inlet. The energy lost as pressure drop is converted to temperature. Notice flow enthalpy conserves because the energy lost does not go anywhere.
-. Temperature rise occurs only in incompressible fluid (liquid)
-. The temperature difference increases as pressure drop increases.